## Slide 1
Cigar-box Violin Project
ENGR 1624 - 12 Fall 2020
Team members:
Cameron Chiaramonte / Design
Nathan Patton / Building
Jose Vallarino / CAD

## Slide 2
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
Maple Wood Cigar Box
Dimensions: 9.75in X 7.00in X 3.44in (L X W X H)
  Wall thickness – 0.25in
  Bottom thickness – 0.25in
  Top thickness – 0.19in
Challenges
  Altering the thickness of the walls of the box in CAD
  Designing and implementing the holes in CAD
  Decided to use a different box

## Slide 3
To perform mode analysis Audacity and Autodesk Inventor were used.
  Inventor used a stress analysis simulation
  Audacity graphed the frequency based off the noise produced from tapping the wood
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014

## Slide 4
Cigar-box Violin Project
ENGR 1620 – XXX Fall 2014
The Original Plan:
The box shown below was our original idea
  A few problems arose
    The box was very small
    The holes were “squeezing” the frequency together and
    only made it worse

## Slide 5
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
New Plan:
The new box was much flatter (dimensions shown on first slide)
The new holes minimized our frequency to our desired range

## Slide 6
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
Chart: Frequency (Hz)
Audacity frequency analysis of the blank box
  Shown below as both the range from Audacity and as a graph from the exported data
  Can see the peak very early on at around 300 Hz

## Slide 7
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
Inventor Stress Analysis of Blank Box
First peak at around 700 Hz

## Slide 8
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
Inventor Stress Analysis of Original and Final Holes
Final holes – first peak at 635.63 Hz
Original holes – 1231.22 Hz

## Slide 9
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
The Product:
Why we chose what we did
  Holes – these holes are very similar to actual f holes
  on a real violin
    They also reduced our frequency more than other holes
    we attempted to use
    Using Professor Williams’ advice we put them in opposite
    corners to further minimize the frequency range

## Slide 10
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
The Product:
Why we chose what we did
  The box
    The flatter box gave much better sound than
    our original small and tall box

## Slide 11
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
The Product:
Why we chose what we did
  The strings
    We used only three strings
      This just worked better with the shape and size
      of our box

## Slide 12
Cigar-box Violin Project
ENGR 1620 – 12 Fall 2014
Our Plan:
CAD the box and find holes that will get us to a desired frequency
Draw and cut out the holes in the box
Make the finger board, the bridge, and the tail piece
Glue on all the pieces from step 3
Attach strings to the violin
Tune